## Slide 1: H HEUER INSTRUMENTS
Based in Sydney, Australia since 1975.
Design and Manufacture of Telecom Test Equipment.
Customer base includes major Telcos, Energy & Power utilities, Infrastructure (Road / Rail / Air), Emergency Services and many others.
Export worldwide

## Slide 2: LT51 Applications
The LT51 Line Tester is a light weight, handheld, battery powered unit suitable for testing in many applications.
200 to 2.2 MHz Bandwidth for VF /Audio and RF analog testing
RF (2 kHz-2.2 MHz) testing of Power Line Carrier (PLC) or xDSL or RF interfaces.
VF (200 Hz to 4 kHz) testing of the PSTN, analog FXS and FXO interfaces of digital exchanges, PCM muxes, microwave radio links or PLC.
Can replace both W&G SPM-3x and PS-3x.

## Slide 3: LT51 Line Tester
DC Power LED
Charging LED
Speaker
Measurement Menu keys
Keypad for dialling and parameter entry
320x240 LCD
Microphone for speakerphone
Backlight control
On/Off key
Knob for cursor, parameter entry, Volume
Soft Keys for menu selection
Save / Enter key
Configuration Menu keys
Battery access

## Slide 4: LT51 Connectors
AC/DC Charger
Transmit signals on this pair
Receive and transmit on this pair, DMM, TDR functions
USB socket for PC connection
Ground

## Slide 5: LT51 features
Selective Level Meter
Spectrum Analyser with zoom
Level Generator (totally independent operation)
DMM - AC/DC voltage, Loop current, nF and 
Return Loss / Impedance Meter
Balance Meter
TDR
POTS – Ring detect, DTMF dialling, handsfree voice

## Slide 6: LT51 Operation
Press the red key to toggle the LT51 ON / OFF.
To force unit OFF, press and hold the key > 5s.
Default setup:
  Separate receiver / transmitter (TX-RX setting or 4-wire)
  Transmitter off
  600  impedance
  Receiver input: bridging
  Receiver Span: 0 – 4.5 kHz
  Total RMS (noise + tones)
  across 4.5 kHz displayed

## Slide 7: Level measurement
Connect the signal to measure to the RTXa-b terminals.
Press the key and set the input impedance by toggling [f1]. Set bridging or terminated, by toggling [f2]
Press [f3] to set auto-range to LVL only.

## Slide 8: Selective Level Meter
Measure level at any frequency from 200 Hz - 2.2 MHz
Press key then [f1]
to select “Level Noise”.
Press key, then [f2]
to set the Centre frequency.
By default the BW is set to 25Hz
for level measurement.
Press [f3] to select a BW of 1.74 or 3.1 kHz for noise measurement.
Cancel Selective mode, by setting BW to “Wide”

## Slide 9: Spectrum Analyser
Zoom in on any frequency up to 2.4 MHz
spans from 4.5, 9.0, 18.0 to 600 kHz, 1.2 & 2.4 MHz
Set up as for Selective Meter, then press key
Use marker to selectively measure level of peaks
Total RMS across span BW (all peaks) is also displayed

## Slide 10: Level Generator
Press the key to change the TX parameters.
Set the output impedance by toggling [f1].
Press [f2] to set the TX level and either use the knob or directly enter a value from -60 to +10 dBm.
Set the TX frequency by pressing [f4], and either use the knob or directly enter a value from 200 Hz to 2.2 MHz.
Press [f3] to toggle the output of a tone SINE or OFF,
Press [f5] to sweep across the set span BW.
Press the key, then [f5] to control whether the tone is output on the Txa-b (TX-RX or 4W mode) or RTXa-b (RTX or 2W mode) terminals.

## Slide 11: Return Loss
Connect the impedance / circuit
to measure to RTXa-b.
Press or key then [f3]
to select Return Loss.
Press key, then [f1] to
setup return loss ref. impedance
Press [f4] to set the frequency,
and either use the knob or directly
enter a value from 200 Hz to 2.2 MHz.
Press [f5] to sweep across span BW.

## Slide 12: DC or AC Voltage
Measure upto 60 Vdc, 33Vrms/ac
Connect the pair to the RTXa-b terminals.
Press the key, then press [f2] to select “Voltage”.
.

## Slide 13: Line Continuity - TDR
TDR is ideal for locating Loop short and open circuits.
Press button for Auto-TDR.
Use cursor for distance to fault.
short
open

## Slide 14: VF Testing (eg. PCM MUX)
Check:
  Idle Channel Noise
  Audio Level Setting
  Frequency Response
  Variation of Gain with input
  level
  Signal to Quantisation Noise
  Cross Talk
  Ring Detect VAC & VDC
  while on-hook
  VDC & IDC when off-hook

## Slide 15: VF Testing (eg. PCM MUX)
Idle Channel Noise
  Press , then [f3] to set the BW to “PSOPH” if required.
  With or without Psophometric weighting
  See User Manual for further set-up options

## Slide 16: VF Testing (eg. PCM MUX)
Audio Level Setting
Use LT51 default setting ( then [f2] to set TERM)
Measure level of received audio tones
See User Manual for details on setting transmitter

## Slide 17: VF Testing (eg. PCM MUX)
Frequency Response
  Single or swept frequency

## Slide 18: VF Testing (eg. PCM MUX)
Variation of Gain with Input Level
See User Manual for details

## Slide 19: VF Testing (eg. PCM MUX)
Signal to Quantisation Noise
  With or without Psophometric filter
  See User Manual for details

## Slide 20: VF Testing (eg. PCM MUX)
Measure Crosstalk in adjacent PCM channels
  Transmit built-in G.227 Telephone Noise signal
  Span = 4.5 kHz, ZRTX = 600
  See User Manual for details

## Slide 21: RF Testing (eg. SSB PLCC)
Transmit VF tone
at 600 ohm from LT51 TXab
into PLCC VF terminal.
Measure RF modulation of
tone onto 500 kHz Carrier
using 50/75 ohm at
LT51 RTXab receive input.
(using supplied BNC Adaptor
to interface to coax)

## Slide 22: PLCC Testing (cont.)
Possible RF Frequency Spectrum for SSB PLCC System
Press then [f2] to set LT51 centre freq. to 498 kHz

## Slide 23: PLCC Testing (cont.)
Typical levels for 3 PLCC SSB frequencies:
* reception level is attenuated by 28dB ± 2 dB
Press to display the frequency spectrum on the LT51
Press [f1] to set the Span to 4.5 kHz for 3 SSB freq.s.
 | Frequency (Hz) | Theoretical level | Measured levels (with 40 dB attenuator)
Tx pilot | 499820 | +26 dBm | -14.00 + 40 = +26 dBm
Rx pilot | 500180 | 0 ± 2 dBm* | -40.00 + 40 = 0 dBm*
External tone (3800 Hz) | 496200 | +32 dBm | -7.98 + 40 = +32 dBm

## Slide 24: PLCC Testing (cont.)
Press to show level at 3 SSB frequencies
Press then
[f2] to set centre
frequency to each SSB frequency.

## Slide 25: Impedance Magnitude
To Disconnector in OPEN position
PLC Line Trap
Line dropper to overhead line
Overhead line must be switched off and earthed by auxiliary earth connection
Make single/swept freq’ncy measurements of impedance
Eg. Measure Line Trap impedances to ensure PLCC signals are restricted / blocked to particular sections of the transmission network

## Slide 26: Return Loss of Coupling Device
Make single/swept freq’ncy measurements of the Return Loss of Coupling Devices or Line Matching Units (LMUs).
Fully automatic measurement with LT51 built-in bridge (no need for external bridges, 0 Ω generator).
Eg. Tuning of LMU (against 75 Ω) to ensure the high frequency carrier signals are sufficiently coupled to the transmission line.
Return Loss should be
> 12 dB over the carrier
freq. BW of interest.

## Slide 27: Save / Recall Measurements
Any current measurement is stored by pressing the key:
  no file system or file names to enter.
  an optional SMS ID string can be attached.
  new results overwrite oldest stored results.
Recall measurements by pressing the key followed by [f1].
Use the knob to select the saved measurement and press [f3] to display the results on the LT51 screen.
Upload measurements to PC using LT51View utility.

## Slide 28: PC Interface
LT51View utility has simple interface for -
  Uploading saved results.
  Download new firmware.
  Remote control via single
  commands or script files